## Slide 1
Gerson Fernando Budke
nandojve@gmail.com
Zephyr Behavior Tree

## Slide 2: Who am I
Zephyr maintainer of:
  Atmel Microcontrollers
    Introduced SAM4E/L SoC devices and drivers
    Introduced SAMV71 SoC devices
  GigaDevice platform
    Introduced the manufacturer
    Introduced the many GD32 SoCs and drivers
  Bouffalo Lab platform
    Introducing the manufacturer https://github.com/zephyrproject-rtos/zephyr/pull/78795
  UpdateHub https://updatehub.io
Many drivers sent to upstream
  USB, I2C, SPI ...
Many drivers fixed
  Ethernet, USB, I2C, SPI ...
Notes: Hook: Celular example
Question: The Application that ran on those phones are the same?

## Slide 3: Agenda
From Baremetal to ZephyrBT
What is Behavior Trees? A brief idea!
ZephyrBT in practice

## Slide 4: From Baremetal to ZephyrBT

## Slide 5
From Baremetal to ZephyrBT
Goals:
  Move from Baremetal to some RTOS
  Flexible platform
  Modular
  Easy to test
  Easy to develop

## Slide 6
From Baremetal to ZephyrBT
Solution:
  Use Zephyr RTOS (very flexible and modular)
  Use Z-Bus (alleviate lot’s of complexity)
  Use RENODE (Make tests easy with a virtual board)
  Keep C language (Developers already know it)
  Keep eyes on Rust in Zephyr (it is the future … )
Still complex!!

## Slide 7: From Baremetal to ZephyrBT

## Slide 8
From Baremetal to ZephyrBT
Organize and split in groups
Z-Bus is lightweight and flexible to manage multiple threads allowing many-to-many communication.

## Slide 9: From Baremetal to ZephyrBT
The Z-Bus expects a sequential flow (no loops allowed)
Easy to implement like an “PLC”
Problem is that you fall into FSM:
    Each new change require at least one new state
    Complexity grows fast
    Difficult to read the logic behind

## Slide 10: From Baremetal to ZephyrBT
So, let’s try something different like behavior trees:
  Sensors can be read only when it is necessary
  It can be easy to share data between nodes
  Fine control of the program execution path
  Program flow is designed graphically
  Easy to extend
  Code is like a Lego !?

## Slide 11: What is Behavior Tree?
A behavior tree is a mathematical model of plan execution used in computer science, robotics, control systems and video games.
Source: Wikipedia

## Slide 12: What is Behavior Tree?
A "good" software architecture should have the following characteristics:
  Modularity
  Reusability of components
  Composability
  Good separation of concerns
Source: BehaviorTree.CPP

## Slide 13: What is Behavior Tree?
Each node (structure) can return one of for status:
  Success (My job is done with Success status)
  Running (I still have work to do)
  Failed (My job is done with Failed status)
  Skip (I don’t have anything to do)

## Slide 14: What is Behavior Tree?
Action node status:
  Could system execute the “Open” action ?
    Yes: return Success
    No: return Fail
  Is the Fridge already “Open” ?
    Yes: return Skip, but it could be Success too
  Is this operation take a lot of time ?
    Yes: return Running and check again on the next round

## Slide 15: What is Behavior Tree?
Sequence Control node status:
For each S in Siblings:
R = Eval(S)
Is the sibling returned Success or Skip?
continue
Return R
  Return Success

## Slide 16: What is Behavior Tree?

## Slide 17: ZephyrBT in practice
The ZephyrBT implementation can be access at
  https://github.com/OSSystems/ZephyrBT
The Groot2 IDE can be download at
  https://www.behaviortree.dev/groot

## Slide 18: ZephyrBT in practice

## Slide 34: Pros
Allow a subset of functions/sub-tree ready on a product
  User can customize their own functions
  User can extend the behavior
  Vendor can hide their IP on a sub-tree
Easy to visualize the data flow

## Slide 35: Cons
Easy to fall in the trap that use too much the blackboard
Blackboard can be evil when used to synchronize between subsystems
Shared data requires synchronization

## Slide 36: Available
Groot2 IDE can be used to develop
ZephyrBT is Apache 2.0
Nodes:
  Actions: Always-Success, Always-Failure, Sleep, Set-Blackboard
  Control: Sequence and Fallback
  Decorators: Inverter, Delay, Repeat, Run-Once, Timeout

## Slide 37: Summary
Behavior Tree is a different development paradigm
ZephyrBT currently is an early stage and implement the minimal
ZephyrBT can be used without an IDE
ZephyrBT is easy to use and cover all the general use cases
ZephyrBT can be easily extended with Custom Actions
ZephyrBT can be extended with other code generators
ZephyrBT is not integrated with ROS
ZephyrBT is not a replacement for BehaviorTree.CPP

## Slide 38: Contact
Gerson Fernando Budke
nandojve@gmail.com

## Slide 39: References
https://www.behaviortree.dev/
BehaviorTree.CPP: Task Planning for Robots and Virtual Agents - Davide Faconti - CppCon 2023
https://github.com/OSSystems/ZephyrBT

## Slide 40: Backup

## Slide 41: ZephyrBT in practice